## Slide 1
Is That a Demo in Your Pocket?
Code Snorpung
Music Nordloef

## Slide 3
The Ultimate
Game Boy Talk
Michael Steil
33C3
2016-12-30
@pagetable
http://www.pagetable.com/

## Slide 4
The Ultimate
Game Boy Talk
Michael Steil
33C3
2016
The Ultimate
Commodore 64 Talk
Michael Steil
25C3
2008
The Ultimate
Atari 2600 Talk
Sven Oliver ('SvOlli') Moll
26C3
2009
The Ultimate
Galaksija Talk
Tomaž Šolc
29C3
2012
The Ultimate
Amiga 500 Talk
rahra
32C3
2015
The Ultimate Talk Series

## Slide 5
1049 Game Boy Games
576 Game Boy Color Games
79 M Game Boy Advance
197 M total
including
Game Boy Advance
1989 - 2009
1989 - 2003
Game Boy &
Game Boy Color
Game Boy &
Game Boy Color
118 M

## Slide 6
Nintendo Game Boy
Apr 1989
NEC TurboExpress
Dec 1990
Atari Lynx
Sep 1989
SEGA Game Gear
Oct 1990
Wikimedia Commons

## Slide 8
Game Boy
Game Boy Pocket
Game Boy Light
Game Boy Color
DMG-01
MGB-001
MGB-101
CGB-001
1989
1996
1998
1998

## Slide 9
AGS-001
AGS-101
Game Boy Advance
Game Boy Advance SP
Game Boy Advance SP
AGB-001
2001
2003
2005

## Slide 10
SHVC-042
SGB2
DOL-017
Super
Game Boy 2
Super
Game Boy
Game Boy Player
SHVC-027
SGB
2003
1994
1998

## Slide 11
66 mm (2.6") Screen
Battery Indicator
Joypad
Speaker

## Slide 12
Link Connector
Volume
External Power
Contrast
Game Pak
On Switch
Headphones

## Slide 14
Game Pak

## Slide 15
Four AA Batteries

## Slide 17
 | Game Boy | NES | Commodore 64 | Atari 2600 | SNES
CPU | 1 MHz* 8 bit | 1.8 MHz 8 bit | 1 MHz 8 bit | 1.2 MHz 8 bit | 3.6 MHz 16 bit
RAM | 8 KB | 2 KB | 64 KB | 0.125 KB | 128 KB
VRAM | 8 KB | 2 KB | 16 KB (shared) | 0 | 64 KB
Resolution | 160x144 | 256x240 | 320x200 | 160x192 | 256x224 512x448
Simultaneous Colors | 4 | 25 | 16 | 128 | 32768
Sprites/Line | 10 | 8 | 8 | 3 | 32
Year | 1989 | 1983 | 1982 | 1977 | 1990

## Slide 23
RAM
VRAM
SoC
DMG
Game Boy

## Slide 24
Super Game Boy
SGB

## Slide 25
Game Boy Pocket
MGB

## Slide 26
Game Boy Light
MGB

## Slide 27
Super Game Boy 2
SGB2

## Slide 28
Game Boy Color
CGB

## Slide 29
GB Boy

## Slide 31
RAM
VRAM
SoC
DMG–CPU

## Slide 32
CPU
Joypad Input
Timer
Serial Data Transfer
Interrupt Controller
Sound Controller
Pixel Processing Unit
Memory
Boot ROM
DMG–CPU

## Slide 33
CPU

## Slide 34
NES
1983
SNES
1990
Game Boy
1989
6502
65816
Wikimedia Commons
LR35902

## Slide 35
LR35902
8080
Z80
1974
1989
http://www.oldcomputers.net/
Wikimedia Commons
1976
Altair 8800
IMSAI 8080
Osborne 1
TRS-80
Spectrum

## Slide 36
unsupported
Z80 features
supported
Z80 features
unsupported
8080 features
new features
supported
core features
Z80
8080
LR35902

## Slide 37
Supported Core Features
Registers | 
A | F
B | C
D | E
H | L
SP | 
PC | 
Flags |  |  |  |  |  |  | 
Z | N | H | C | - | - | - | -
*
* different layout than 8080
A
F
B
C
D
E
H
L
BC | 
DE | 
HL | 
a
b
c
d
e
h
l
(hl)
r8
bc
de
hl
sp
r16

## Slide 38
Supported Core Features
add
adc
sub
sbc
and
xor
or
cp
inc
dec
daa
cpl
add hl, r16
inc r16
dec r16
a, d8
a, r8
r8
Artih/Logical
ld sp, hl
push r16
pop r16
Stack
Rotate
rlca
rla
rrca
rra
ccf
scf
nop
halt
di
ei
Rotate
Rotate
Misc
jp a16
jp hl
jp f, a16
call a16
call f, a16
ret
ret f
rst n
Control Flow
ld r8, d8
ld r8, r8
ld a, (bc)
ld a, (de)
ld a, (a16)
ld (bc), a
ld (de), a
ld (a16), a
ld r16, d16
Load/Store
*
*
* different opcode than 8080
Registers | 
A | F
B | C
D | E
H | L
SP | 
PC | 
a (hl)
b c
d e
h l
r8
bc
de
hl
sp
r16

## Slide 39
0000
0008
0010
0018
0020
0028
0030
0038
0040
0048
0050
0058
0060
.
.
.
rst $00
rst $08
rst $10
rst $18
rst $20
rst $28
rst $30
rst $38
irq service routine #0
irq service routine #1
irq service routine #2
irq service routine #3
irq service routine #4
RESET
Supported Core Features

## Slide 40
Unsupported 8080 Features
ret po
jp
call
ret pe
jp
call
ret p
jp
call
ret m
jp
call
Sign & Parity
po, nn
pe, nn
p, nn
m, nn
ex (sp), hl
ex de, hl
Exchange
out (a8), a
in a, (a8)
Port I/O
ld (a16), hl
ld hl, (a16)
Load/Store HL
Flags |  |  |  |  |  |  | 
Z | N | H | C | - | - | - | -
Flags |  |  |  |  |  |  | 
S | Z | - | H | - | P | - | C
X
X

## Slide 41
Supported Z80 Features
jr a8
jr nz, a8
jr z, a8
jr nc, a8
jr c, a8
Relative Jump
reti
Interrupt Return
*
* different opcode than Z80
rlc r8
rl r8
rrc r8
rr r8
sla r8
sra r8
srl r8
bit n, r8
set n, r8
res n, r8
Shift & Bit Ops
CB Prefix

## Slide 42
A’ | F’
B’ | C’
D’ | E’
H’ | L’
Registers | 
A | F
B | C
D | E
H | L
SP | 
PC | 
Unsupported Z80 Features
ex af, af'
exx
Alternate Regs
ld r16, (a16)
ld (a16), r16
Load/Store 16b
adc hl, r16
sbc hl, r16
neg
Arithmetic
IX | 
IY | 
im 0/1/2
ld a, i
ld i, a
ld a, r
ld r, a
SPR
cpi/cpir/cpd/cpdr
ini/inir/ind/indr
outi/outir/outd/outr
ldi/ldir/ldd/lddr
djnz
Auto-Inc/Dec, Loop
rld
rrd
4-bit Rotate
retn
Control Flow
X
X
X
X

## Slide 43
New Features
ld (hl+), a
ld a, (hl+)
ld (hl-), a
ld a, (hl-)
Postinc/Predec
mem[hl] = a; hl++;
a = mem[hl]; hl++;
hl--; mem[hl] = a;
hl--; a = mem[hl];

## Slide 44
New Features
ld ($ff00+a8), a
ld a, ($ff00+a8)
ld ($ff00+c), a
ld a, ($ff00+c)
Zero Page
0 KB
64 KB
fa 40 ff ld a, ($ff40) 4 cycles
f0 40 ld a, ($ff40) 3 cycles
FF00
FFFF

## Slide 45
New Features
stop
Power Saving
swap r8
Swap Nibbles
add sp, r8
ld hl, sp+r8
Stack
* Z80 has a more generic version
ld (a16), sp
Store SP
*

## Slide 46
 | x0 | x1 | x2 | x3 | x4 | x5 | x6 | x7 | x8 | x9 | xA | xB | xC | xD | xE | xF
0x | NOP 1 4 - - - - | LD BC,d16 3 12 - - - - | LD (BC),A 1 8 - - - - | INC BC 1 8 - - - - | INC B 1 4 Z 0 H - | DEC B 1 4 Z 1 H - | LD B,d8 2 8 - - - - | RLCA 1 4 0 0 0 C | LD (a16),SP 3 20 - - - - | ADD HL,BC 1 8 - 0 H C | LD A,(BC) 1 8 - - - - | DEC BC 1 8 - - - - | INC C 1 4 Z 0 H - | DEC C 1 4 Z 1 H - | LD C,d8 2 8 - - - - | RRCA 1 4 0 0 0 C
1x | STOP 0 2 4 - - - - | LD DE,d16 3 12 - - - - | LD (DE),A 1 8 - - - - | INC DE 1 8 - - - - | INC D 1 4 Z 0 H - | DEC D 1 4 Z 1 H - | LD D,d8 2 8 - - - - | RLA 1 4 0 0 0 C | JR r8 2 12 - - - - | ADD HL,DE 1 8 - 0 H C | LD A,(DE) 1 8 - - - - | DEC DE 1 8 - - - - | INC E 1 4 Z 0 H - | DEC E 1 4 Z 1 H - | LD E,d8 2 8 - - - - | RRA 1 4 0 0 0 C
2x | JR NZ,r8 2 12/8 - - - - | LD HL,d16 3 12 - - - - | LD (HL+),A 1 8 - - - - | INC HL 1 8 - - - - | INC H 1 4 Z 0 H - | DEC H 1 4 Z 1 H - | LD H,d8 2 8 - - - - | DAA 1 4 Z - 0 C | JR Z,r8 2 12/8 - - - - | ADD HL,HL 1 8 - 0 H C | LD A,(HL+) 1 8 - - - - | DEC HL 1 8 - - - - | INC L 1 4 Z 0 H - | DEC L 1 4 Z 1 H - | LD L,d8 2 8 - - - - | CPL 1 4 - 1 1 -
3x | JR NC,r8 2 12/8 - - - - | LD SP,d16 3 12 - - - - | LD (HL-),A 1 8 - - - - | INC SP 1 8 - - - - | INC (HL) 1 12 Z 0 H - | DEC (HL) 1 12 Z 1 H - | LD (HL),d8 2 12 - - - - | SCF 1 4 - 0 0 1 | JR C,r8 2 12/8 - - - - | ADD HL,SP 1 8 - 0 H C | LD A,(HL-) 1 8 - - - - | DEC SP 1 8 - - - - | INC A 1 4 Z 0 H - | DEC A 1 4 Z 1 H - | LD A,d8 2 8 - - - - | CCF 1 4 - 0 0 C
4x | LD B,B 1 4 - - - - | LD B,C 1 4 - - - - | LD B,D 1 4 - - - - | LD B,E 1 4 - - - - | LD B,H 1 4 - - - - | LD B,L 1 4 - - - - | LD B,(HL) 1 8 - - - - | LD B,A 1 4 - - - - | LD C,B 1 4 - - - - | LD C,C 1 4 - - - - | LD C,D 1 4 - - - - | LD C,E 1 4 - - - - | LD C,H 1 4 - - - - | LD C,L 1 4 - - - - | LD C,(HL) 1 8 - - - - | LD C,A 1 4 - - - -
5x | LD D,B 1 4 - - - - | LD D,C 1 4 - - - - | LD D,D 1 4 - - - - | LD D,E 1 4 - - - - | LD D,H 1 4 - - - - | LD D,L 1 4 - - - - | LD D,(HL) 1 8 - - - - | LD D,A 1 4 - - - - | LD E,B 1 4 - - - - | LD E,C 1 4 - - - - | LD E,D 1 4 - - - - | LD E,E 1 4 - - - - | LD E,H 1 4 - - - - | LD E,L 1 4 - - - - | LD E,(HL) 1 8 - - - - | LD E,A 1 4 - - - -
6x | LD H,B 1 4 - - - - | LD H,C 1 4 - - - - | LD H,D 1 4 - - - - | LD H,E 1 4 - - - - | LD H,H 1 4 - - - - | LD H,L 1 4 - - - - | LD H,(HL) 1 8 - - - - | LD H,A 1 4 - - - - | LD L,B 1 4 - - - - | LD L,C 1 4 - - - - | LD L,D 1 4 - - - - | LD L,E 1 4 - - - - | LD L,H 1 4 - - - - | LD L,L 1 4 - - - - | LD L,(HL) 1 8 - - - - | LD L,A 1 4 - - - -
7x | LD (HL),B 1 8 - - - - | LD (HL),C 1 8 - - - - | LD (HL),D 1 8 - - - - | LD (HL),E 1 8 - - - - | LD (HL),H 1 8 - - - - | LD (HL),L 1 8 - - - - | HALT 1 4 - - - - | LD (HL),A 1 8 - - - - | LD A,B 1 4 - - - - | LD A,C 1 4 - - - - | LD A,D 1 4 - - - - | LD A,E 1 4 - - - - | LD A,H 1 4 - - - - | LD A,L 1 4 - - - - | LD A,(HL) 1 8 - - - - | LD A,A 1 4 - - - -
8x | ADD A,B 1 4 Z 0 H C | ADD A,C 1 4 Z 0 H C | ADD A,D 1 4 Z 0 H C | ADD A,E 1 4 Z 0 H C | ADD A,H 1 4 Z 0 H C | ADD A,L 1 4 Z 0 H C | ADD A,(HL) 1 8 Z 0 H C | ADD A,A 1 4 Z 0 H C | ADC A,B 1 4 Z 0 H C | ADC A,C 1 4 Z 0 H C | ADC A,D 1 4 Z 0 H C | ADC A,E 1 4 Z 0 H C | ADC A,H 1 4 Z 0 H C | ADC A,L 1 4 Z 0 H C | ADC A,(HL) 1 8 Z 0 H C | ADC A,A 1 4 Z 0 H C
9x | SUB B 1 4 Z 1 H C | SUB C 1 4 Z 1 H C | SUB D 1 4 Z 1 H C | SUB E 1 4 Z 1 H C | SUB H 1 4 Z 1 H C | SUB L 1 4 Z 1 H C | SUB (HL) 1 8 Z 1 H C | SUB A 1 4 Z 1 H C | SBC A,B 1 4 Z 1 H C | SBC A,C 1 4 Z 1 H C | SBC A,D 1 4 Z 1 H C | SBC A,E 1 4 Z 1 H C | SBC A,H 1 4 Z 1 H C | SBC A,L 1 4 Z 1 H C | SBC A,(HL) 1 8 Z 1 H C | SBC A,A 1 4 Z 1 H C
Ax | AND B 1 4 Z 0 1 0 | AND C 1 4 Z 0 1 0 | AND D 1 4 Z 0 1 0 | AND E 1 4 Z 0 1 0 | AND H 1 4 Z 0 1 0 | AND L 1 4 Z 0 1 0 | AND (HL) 1 8 Z 0 1 0 | AND A 1 4 Z 0 1 0 | XOR B 1 4 Z 0 0 0 | XOR C 1 4 Z 0 0 0 | XOR D 1 4 Z 0 0 0 | XOR E 1 4 Z 0 0 0 | XOR H 1 4 Z 0 0 0 | XOR L 1 4 Z 0 0 0 | XOR (HL) 1 8 Z 0 0 0 | XOR A 1 4 Z 0 0 0
Bx | OR B 1 4 Z 0 0 0 | OR C 1 4 Z 0 0 0 | OR D 1 4 Z 0 0 0 | OR E 1 4 Z 0 0 0 | OR H 1 4 Z 0 0 0 | OR L 1 4 Z 0 0 0 | OR (HL) 1 8 Z 0 0 0 | OR A 1 4 Z 0 0 0 | CP B 1 4 Z 1 H C | CP C 1 4 Z 1 H C | CP D 1 4 Z 1 H C | CP E 1 4 Z 1 H C | CP H 1 4 Z 1 H C | CP L 1 4 Z 1 H C | CP (HL) 1 8 Z 1 H C | CP A 1 4 Z 1 H C
Cx | RET NZ 1 20/8 - - - - | POP BC 1 12 - - - - | JP NZ,a16 3 16/12 - - - - | JP a16 3 16 - - - - | CALL NZ,a16 3 24/12 - - - - | PUSH BC 1 16 - - - - | ADD A,d8 2 8 Z 0 H C | RST 00H 1 16 - - - - | RET Z 1 20/8 - - - - | RET 1 16 - - - - | JP Z,a16 3 16/12 - - - - | PREFIX CB 1 4 - - - - | CALL Z,a16 3 24/12 - - - - | CALL a16 3 24 - - - - | ADC A,d8 2 8 Z 0 H C | RST 08H 1 16 - - - -
Dx | RET NC 1 20/8 - - - - | POP DE 1 12 - - - - | JP NC,a16 3 16/12 - - - - |  | CALL NC,a16 3 24/12 - - - - | PUSH DE 1 16 - - - - | SUB d8 2 8 Z 1 H C | RST 10H 1 16 - - - - | RET C 1 20/8 - - - - | RETI 1 16 - - - - | JP C,a16 3 16/12 - - - - |  | CALL C,a16 3 24/12 - - - - |  | SBC A,d8 2 8 Z 1 H C | RST 18H 1 16 - - - -
Ex | LDH (a8),A 2 12 - - - - | POP HL 1 12 - - - - | LD (C),A 2 8 - - - - |  |  | PUSH HL 1 16 - - - - | AND d8 2 8 Z 0 1 0 | RST 20H 1 16 - - - - | ADD SP,r8 2 16 0 0 H C | JP (HL) 1 4 - - - - | LD (a16),A 3 16 - - - - |  |  |  | XOR d8 2 8 Z 0 0 0 | RST 28H 1 16 - - - -
Fx | LDH A,(a8) 2 12 - - - - | POP AF 1 12 Z N H C | LD A,(C) 2 8 - - - - | DI 1 4 - - - - |  | PUSH AF 1 16 - - - - | OR d8 2 8 Z 0 0 0 | RST 30H 1 16 - - - - | LD HL,SP+r8 2 12 0 0 H C | LD SP,HL 1 8 - - - - | LD A,(a16) 3 16 - - - - | EI 1 4 - - - - |  |  | CP d8 2 8 Z 1 H C | RST 38H 1 16 - - - -
http://pastraiser.com
PREFIX CB 1 4 - - - -

## Slide 47
http://pastraiser.com
 | x0 | x1 | x2 | x3 | x4 | x5 | x6 | x7 | x8 | x9 | xA | xB | xC | xD | xE | xF
0x | RLC B 2 8 Z 0 0 C | RLC C 2 8 Z 0 0 C | RLC D 2 8 Z 0 0 C | RLC E 2 8 Z 0 0 C | RLC H 2 8 Z 0 0 C | RLC L 2 8 Z 0 0 C | RLC (HL) 2 16 Z 0 0 C | RLC A 2 8 Z 0 0 C | RRC B 2 8 Z 0 0 C | RRC C 2 8 Z 0 0 C | RRC D 2 8 Z 0 0 C | RRC E 2 8 Z 0 0 C | RRC H 2 8 Z 0 0 C | RRC L 2 8 Z 0 0 C | RRC (HL) 2 16 Z 0 0 C | RRC A 2 8 Z 0 0 C
1x | RL B 2 8 Z 0 0 C | RL C 2 8 Z 0 0 C | RL D 2 8 Z 0 0 C | RL E 2 8 Z 0 0 C | RL H 2 8 Z 0 0 C | RL L 2 8 Z 0 0 C | RL (HL) 2 16 Z 0 0 C | RL A 2 8 Z 0 0 C | RR B 2 8 Z 0 0 C | RR C 2 8 Z 0 0 C | RR D 2 8 Z 0 0 C | RR E 2 8 Z 0 0 C | RR H 2 8 Z 0 0 C | RR L 2 8 Z 0 0 C | RR (HL) 2 16 Z 0 0 C | RR A 2 8 Z 0 0 C
2x | SLA B 2 8 Z 0 0 C | SLA C 2 8 Z 0 0 C | SLA D 2 8 Z 0 0 C | SLA E 2 8 Z 0 0 C | SLA H 2 8 Z 0 0 C | SLA L 2 8 Z 0 0 C | SLA (HL) 2 16 Z 0 0 C | SLA A 2 8 Z 0 0 C | SRA B 2 8 Z 0 0 0 | SRA C 2 8 Z 0 0 0 | SRA D 2 8 Z 0 0 0 | SRA E 2 8 Z 0 0 0 | SRA H 2 8 Z 0 0 0 | SRA L 2 8 Z 0 0 0 | SRA (HL) 2 16 Z 0 0 0 | SRA A 2 8 Z 0 0 0
3x | SWAP B 2 8 Z 0 0 0 | SWAP C 2 8 Z 0 0 0 | SWAP D 2 8 Z 0 0 0 | SWAP E 2 8 Z 0 0 0 | SWAP H 2 8 Z 0 0 0 | SWAP L 2 8 Z 0 0 0 | SWAP (HL) 2 16 Z 0 0 0 | SWAP A 2 8 Z 0 0 0 | SRL B 2 8 Z 0 0 C | SRL C 2 8 Z 0 0 C | SRL D 2 8 Z 0 0 C | SRL E 2 8 Z 0 0 C | SRL H 2 8 Z 0 0 C | SRL L 2 8 Z 0 0 C | SRL (HL) 2 16 Z 0 0 C | SRL A 2 8 Z 0 0 C
4x | BIT 0,B 2 8 Z 0 1 - | BIT 0,C 2 8 Z 0 1 - | BIT 0,D 2 8 Z 0 1 - | BIT 0,E 2 8 Z 0 1 - | BIT 0,H 2 8 Z 0 1 - | BIT 0,L 2 8 Z 0 1 - | BIT 0,(HL) 2 16 Z 0 1 - | BIT 0,A 2 8 Z 0 1 - | BIT 1,B 2 8 Z 0 1 - | BIT 1,C 2 8 Z 0 1 - | BIT 1,D 2 8 Z 0 1 - | BIT 1,E 2 8 Z 0 1 - | BIT 1,H 2 8 Z 0 1 - | BIT 1,L 2 8 Z 0 1 - | BIT 1,(HL) 2 16 Z 0 1 - | BIT 1,A 2 8 Z 0 1 -
5x | BIT 2,B 2 8 Z 0 1 - | BIT 2,C 2 8 Z 0 1 - | BIT 2,D 2 8 Z 0 1 - | BIT 2,E 2 8 Z 0 1 - | BIT 2,H 2 8 Z 0 1 - | BIT 2,L 2 8 Z 0 1 - | BIT 2,(HL) 2 16 Z 0 1 - | BIT 2,A 2 8 Z 0 1 - | BIT 3,B 2 8 Z 0 1 - | BIT 3,C 2 8 Z 0 1 - | BIT 3,D 2 8 Z 0 1 - | BIT 3,E 2 8 Z 0 1 - | BIT 3,H 2 8 Z 0 1 - | BIT 3,L 2 8 Z 0 1 - | BIT 3,(HL) 2 16 Z 0 1 - | BIT 3,A 2 8 Z 0 1 -
6x | BIT 4,B 2 8 Z 0 1 - | BIT 4,C 2 8 Z 0 1 - | BIT 4,D 2 8 Z 0 1 - | BIT 4,E 2 8 Z 0 1 - | BIT 4,H 2 8 Z 0 1 - | BIT 4,L 2 8 Z 0 1 - | BIT 4,(HL) 2 16 Z 0 1 - | BIT 4,A 2 8 Z 0 1 - | BIT 5,B 2 8 Z 0 1 - | BIT 5,C 2 8 Z 0 1 - | BIT 5,D 2 8 Z 0 1 - | BIT 5,E 2 8 Z 0 1 - | BIT 5,H 2 8 Z 0 1 - | BIT 5,L 2 8 Z 0 1 - | BIT 5,(HL) 2 16 Z 0 1 - | BIT 5,A 2 8 Z 0 1 -
7x | BIT 6,B 2 8 Z 0 1 - | BIT 6,C 2 8 Z 0 1 - | BIT 6,D 2 8 Z 0 1 - | BIT 6,E 2 8 Z 0 1 - | BIT 6,H 2 8 Z 0 1 - | BIT 6,L 2 8 Z 0 1 - | BIT 6,(HL) 2 16 Z 0 1 - | BIT 6,A 2 8 Z 0 1 - | BIT 7,B 2 8 Z 0 1 - | BIT 7,C 2 8 Z 0 1 - | BIT 7,D 2 8 Z 0 1 - | BIT 7,E 2 8 Z 0 1 - | BIT 7,H 2 8 Z 0 1 - | BIT 7,L 2 8 Z 0 1 - | BIT 7,(HL) 2 16 Z 0 1 - | BIT 7,A 2 8 Z 0 1 -
8x | RES 0,B 2 8 - - - - | RES 0,C 2 8 - - - - | RES 0,D 2 8 - - - - | RES 0,E 2 8 - - - - | RES 0,H 2 8 - - - - | RES 0,L 2 8 - - - - | RES 0,(HL) 2 16 - - - - | RES 0,A 2 8 - - - - | RES 1,B 2 8 - - - - | RES 1,C 2 8 - - - - | RES 1,D 2 8 - - - - | RES 1,E 2 8 - - - - | RES 1,H 2 8 - - - - | RES 1,L 2 8 - - - - | RES 1,(HL) 2 16 - - - - | RES 1,A 2 8 - - - -
9x | RES 2,B 2 8 - - - - | RES 2,C 2 8 - - - - | RES 2,D 2 8 - - - - | RES 2,E 2 8 - - - - | RES 2,H 2 8 - - - - | RES 2,L 2 8 - - - - | RES 2,(HL) 2 16 - - - - | RES 2,A 2 8 - - - - | RES 3,B 2 8 - - - - | RES 3,C 2 8 - - - - | RES 3,D 2 8 - - - - | RES 3,E 2 8 - - - - | RES 3,H 2 8 - - - - | RES 3,L 2 8 - - - - | RES 3,(HL) 2 16 - - - - | RES 3,A 2 8 - - - -
Ax | RES 4,B 2 8 - - - - | RES 4,C 2 8 - - - - | RES 4,D 2 8 - - - - | RES 4,E 2 8 - - - - | RES 4,H 2 8 - - - - | RES 4,L 2 8 - - - - | RES 4,(HL) 2 16 - - - - | RES 4,A 2 8 - - - - | RES 5,B 2 8 - - - - | RES 5,C 2 8 - - - - | RES 5,D 2 8 - - - - | RES 5,E 2 8 - - - - | RES 5,H 2 8 - - - - | RES 5,L 2 8 - - - - | RES 5,(HL) 2 16 - - - - | RES 5,A 2 8 - - - -
Bx | RES 6,B 2 8 - - - - | RES 6,C 2 8 - - - - | RES 6,D 2 8 - - - - | RES 6,E 2 8 - - - - | RES 6,H 2 8 - - - - | RES 6,L 2 8 - - - - | RES 6,(HL) 2 16 - - - - | RES 6,A 2 8 - - - - | RES 7,B 2 8 - - - - | RES 7,C 2 8 - - - - | RES 7,D 2 8 - - - - | RES 7,E 2 8 - - - - | RES 7,H 2 8 - - - - | RES 7,L 2 8 - - - - | RES 7,(HL) 2 16 - - - - | RES 7,A 2 8 - - - -
Cx | SET 0,B 2 8 - - - - | SET 0,C 2 8 - - - - | SET 0,D 2 8 - - - - | SET 0,E 2 8 - - - - | SET 0,H 2 8 - - - - | SET 0,L 2 8 - - - - | SET 0,(HL) 2 16 - - - - | SET 0,A 2 8 - - - - | SET 1,B 2 8 - - - - | SET 1,C 2 8 - - - - | SET 1,D 2 8 - - - - | SET 1,E 2 8 - - - - | SET 1,H 2 8 - - - - | SET 1,L 2 8 - - - - | SET 1,(HL) 2 16 - - - - | SET 1,A 2 8 - - - -
Dx | SET 2,B 2 8 - - - - | SET 2,C 2 8 - - - - | SET 2,D 2 8 - - - - | SET 2,E 2 8 - - - - | SET 2,H 2 8 - - - - | SET 2,L 2 8 - - - - | SET 2,(HL) 2 16 - - - - | SET 2,A 2 8 - - - - | SET 3,B 2 8 - - - - | SET 3,C 2 8 - - - - | SET 3,D 2 8 - - - - | SET 3,E 2 8 - - - - | SET 3,H 2 8 - - - - | SET 3,L 2 8 - - - - | SET 3,(HL) 2 16 - - - - | SET 3,A 2 8 - - - -
Ex | SET 4,B 2 8 - - - - | SET 4,C 2 8 - - - - | SET 4,D 2 8 - - - - | SET 4,E 2 8 - - - - | SET 4,H 2 8 - - - - | SET 4,L 2 8 - - - - | SET 4,(HL) 2 16 - - - - | SET 4,A 2 8 - - - - | SET 5,B 2 8 - - - - | SET 5,C 2 8 - - - - | SET 5,D 2 8 - - - - | SET 5,E 2 8 - - - - | SET 5,H 2 8 - - - - | SET 5,L 2 8 - - - - | SET 5,(HL) 2 16 - - - - | SET 5,A 2 8 - - - -
Fx | SET 6,B 2 8 - - - - | SET 6,C 2 8 - - - - | SET 6,D 2 8 - - - - | SET 6,E 2 8 - - - - | SET 6,H 2 8 - - - - | SET 6,L 2 8 - - - - | SET 6,(HL) 2 16 - - - - | SET 6,A 2 8 - - - - | SET 7,B 2 8 - - - - | SET 7,C 2 8 - - - - | SET 7,D 2 8 - - - - | SET 7,E 2 8 - - - - | SET 7,H 2 8 - - - - | SET 7,L 2 8 - - - - | SET 7,(HL) 2 16 - - - - | SET 7,A 2 8 - - - -
CB

## Slide 48
 | x0 | x1 | x2 | x3 | x4 | x5 | x6 | x7 | x8 | x9 | xA | xB | xC | xD | xE | xF
0x | NOP 1 4 - - - - | LD BC,d16 3 12 - - - - | LD (BC),A 1 8 - - - - | INC BC 1 8 - - - - | INC B 1 4 Z 0 H - | DEC B 1 4 Z 1 H - | LD B,d8 2 8 - - - - | RLCA 1 4 0 0 0 C | LD (a16),SP 3 20 - - - - | ADD HL,BC 1 8 - 0 H C | LD A,(BC) 1 8 - - - - | DEC BC 1 8 - - - - | INC C 1 4 Z 0 H - | DEC C 1 4 Z 1 H - | LD C,d8 2 8 - - - - | RRCA 1 4 0 0 0 C
1x | STOP 0 2 4 - - - - | LD DE,d16 3 12 - - - - | LD (DE),A 1 8 - - - - | INC DE 1 8 - - - - | INC D 1 4 Z 0 H - | DEC D 1 4 Z 1 H - | LD D,d8 2 8 - - - - | RLA 1 4 0 0 0 C | JR r8 2 12 - - - - | ADD HL,DE 1 8 - 0 H C | LD A,(DE) 1 8 - - - - | DEC DE 1 8 - - - - | INC E 1 4 Z 0 H - | DEC E 1 4 Z 1 H - | LD E,d8 2 8 - - - - | RRA 1 4 0 0 0 C
2x | JR NZ,r8 2 12/8 - - - - | LD HL,d16 3 12 - - - - | LD (HL+),A 1 8 - - - - | INC HL 1 8 - - - - | INC H 1 4 Z 0 H - | DEC H 1 4 Z 1 H - | LD H,d8 2 8 - - - - | DAA 1 4 Z - 0 C | JR Z,r8 2 12/8 - - - - | ADD HL,HL 1 8 - 0 H C | LD A,(HL+) 1 8 - - - - | DEC HL 1 8 - - - - | INC L 1 4 Z 0 H - | DEC L 1 4 Z 1 H - | LD L,d8 2 8 - - - - | CPL 1 4 - 1 1 -
3x | JR NC,r8 2 12/8 - - - - | LD SP,d16 3 12 - - - - | LD (HL-),A 1 8 - - - - | INC SP 1 8 - - - - | INC (HL) 1 12 Z 0 H - | DEC (HL) 1 12 Z 1 H - | LD (HL),d8 2 12 - - - - | SCF 1 4 - 0 0 1 | JR C,r8 2 12/8 - - - - | ADD HL,SP 1 8 - 0 H C | LD A,(HL-) 1 8 - - - - | DEC SP 1 8 - - - - | INC A 1 4 Z 0 H - | DEC A 1 4 Z 1 H - | LD A,d8 2 8 - - - - | CCF 1 4 - 0 0 C
4x | LD B,B 1 4 - - - - | LD B,C 1 4 - - - - | LD B,D 1 4 - - - - | LD B,E 1 4 - - - - | LD B,H 1 4 - - - - | LD B,L 1 4 - - - - | LD B,(HL) 1 8 - - - - | LD B,A 1 4 - - - - | LD C,B 1 4 - - - - | LD C,C 1 4 - - - - | LD C,D 1 4 - - - - | LD C,E 1 4 - - - - | LD C,H 1 4 - - - - | LD C,L 1 4 - - - - | LD C,(HL) 1 8 - - - - | LD C,A 1 4 - - - -
5x | LD D,B 1 4 - - - - | LD D,C 1 4 - - - - | LD D,D 1 4 - - - - | LD D,E 1 4 - - - - | LD D,H 1 4 - - - - | LD D,L 1 4 - - - - | LD D,(HL) 1 8 - - - - | LD D,A 1 4 - - - - | LD E,B 1 4 - - - - | LD E,C 1 4 - - - - | LD E,D 1 4 - - - - | LD E,E 1 4 - - - - | LD E,H 1 4 - - - - | LD E,L 1 4 - - - - | LD E,(HL) 1 8 - - - - | LD E,A 1 4 - - - -
6x | LD H,B 1 4 - - - - | LD H,C 1 4 - - - - | LD H,D 1 4 - - - - | LD H,E 1 4 - - - - | LD H,H 1 4 - - - - | LD H,L 1 4 - - - - | LD H,(HL) 1 8 - - - - | LD H,A 1 4 - - - - | LD L,B 1 4 - - - - | LD L,C 1 4 - - - - | LD L,D 1 4 - - - - | LD L,E 1 4 - - - - | LD L,H 1 4 - - - - | LD L,L 1 4 - - - - | LD L,(HL) 1 8 - - - - | LD L,A 1 4 - - - -
7x | LD (HL),B 1 8 - - - - | LD (HL),C 1 8 - - - - | LD (HL),D 1 8 - - - - | LD (HL),E 1 8 - - - - | LD (HL),H 1 8 - - - - | LD (HL),L 1 8 - - - - | HALT 1 4 - - - - | LD (HL),A 1 8 - - - - | LD A,B 1 4 - - - - | LD A,C 1 4 - - - - | LD A,D 1 4 - - - - | LD A,E 1 4 - - - - | LD A,H 1 4 - - - - | LD A,L 1 4 - - - - | LD A,(HL) 1 8 - - - - | LD A,A 1 4 - - - -
8x | ADD A,B 1 4 Z 0 H C | ADD A,C 1 4 Z 0 H C | ADD A,D 1 4 Z 0 H C | ADD A,E 1 4 Z 0 H C | ADD A,H 1 4 Z 0 H C | ADD A,L 1 4 Z 0 H C | ADD A,(HL) 1 8 Z 0 H C | ADD A,A 1 4 Z 0 H C | ADC A,B 1 4 Z 0 H C | ADC A,C 1 4 Z 0 H C | ADC A,D 1 4 Z 0 H C | ADC A,E 1 4 Z 0 H C | ADC A,H 1 4 Z 0 H C | ADC A,L 1 4 Z 0 H C | ADC A,(HL) 1 8 Z 0 H C | ADC A,A 1 4 Z 0 H C
9x | SUB B 1 4 Z 1 H C | SUB C 1 4 Z 1 H C | SUB D 1 4 Z 1 H C | SUB E 1 4 Z 1 H C | SUB H 1 4 Z 1 H C | SUB L 1 4 Z 1 H C | SUB (HL) 1 8 Z 1 H C | SUB A 1 4 Z 1 H C | SBC A,B 1 4 Z 1 H C | SBC A,C 1 4 Z 1 H C | SBC A,D 1 4 Z 1 H C | SBC A,E 1 4 Z 1 H C | SBC A,H 1 4 Z 1 H C | SBC A,L 1 4 Z 1 H C | SBC A,(HL) 1 8 Z 1 H C | SBC A,A 1 4 Z 1 H C
Ax | AND B 1 4 Z 0 1 0 | AND C 1 4 Z 0 1 0 | AND D 1 4 Z 0 1 0 | AND E 1 4 Z 0 1 0 | AND H 1 4 Z 0 1 0 | AND L 1 4 Z 0 1 0 | AND (HL) 1 8 Z 0 1 0 | AND A 1 4 Z 0 1 0 | XOR B 1 4 Z 0 0 0 | XOR C 1 4 Z 0 0 0 | XOR D 1 4 Z 0 0 0 | XOR E 1 4 Z 0 0 0 | XOR H 1 4 Z 0 0 0 | XOR L 1 4 Z 0 0 0 | XOR (HL) 1 8 Z 0 0 0 | XOR A 1 4 Z 0 0 0
Bx | OR B 1 4 Z 0 0 0 | OR C 1 4 Z 0 0 0 | OR D 1 4 Z 0 0 0 | OR E 1 4 Z 0 0 0 | OR H 1 4 Z 0 0 0 | OR L 1 4 Z 0 0 0 | OR (HL) 1 8 Z 0 0 0 | OR A 1 4 Z 0 0 0 | CP B 1 4 Z 1 H C | CP C 1 4 Z 1 H C | CP D 1 4 Z 1 H C | CP E 1 4 Z 1 H C | CP H 1 4 Z 1 H C | CP L 1 4 Z 1 H C | CP (HL) 1 8 Z 1 H C | CP A 1 4 Z 1 H C
Cx | RET NZ 1 20/8 - - - - | POP BC 1 12 - - - - | JP NZ,a16 3 16/12 - - - - | JP a16 3 16 - - - - | CALL NZ,a16 3 24/12 - - - - | PUSH BC 1 16 - - - - | ADD A,d8 2 8 Z 0 H C | RST 00H 1 16 - - - - | RET Z 1 20/8 - - - - | RET 1 16 - - - - | JP Z,a16 3 16/12 - - - - | PREFIX CB 1 4 - - - - | CALL Z,a16 3 24/12 - - - - | CALL a16 3 24 - - - - | ADC A,d8 2 8 Z 0 H C | RST 08H 1 16 - - - -
Dx | RET NC 1 20/8 - - - - | POP DE 1 12 - - - - | JP NC,a16 3 16/12 - - - - |  | CALL NC,a16 3 24/12 - - - - | PUSH DE 1 16 - - - - | SUB d8 2 8 Z 1 H C | RST 10H 1 16 - - - - | RET C 1 20/8 - - - - | RETI 1 16 - - - - | JP C,a16 3 16/12 - - - - |  | CALL C,a16 3 24/12 - - - - |  | SBC A,d8 2 8 Z 1 H C | RST 18H 1 16 - - - -
Ex | LDH (a8),A 2 12 - - - - | POP HL 1 12 - - - - | LD (C),A 2 8 - - - - |  |  | PUSH HL 1 16 - - - - | AND d8 2 8 Z 0 1 0 | RST 20H 1 16 - - - - | ADD SP,r8 2 16 0 0 H C | JP (HL) 1 4 - - - - | LD (a16),A 3 16 - - - - |  |  |  | XOR d8 2 8 Z 0 0 0 | RST 28H 1 16 - - - -
Fx | LDH A,(a8) 2 12 - - - - | POP AF 1 12 Z N H C | LD A,(C) 2 8 - - - - | DI 1 4 - - - - |  | PUSH AF 1 16 - - - - | OR d8 2 8 Z 0 0 0 | RST 30H 1 16 - - - - | LD HL,SP+r8 2 12 0 0 H C | LD SP,HL 1 8 - - - - | LD A,(a16) 3 16 - - - - | EI 1 4 - - - - |  |  | CP d8 2 8 Z 1 H C | RST 38H 1 16 - - - -
http://pastraiser.com
LD A,(a16) 3 16 - - - -
bytes
clocks
@ 4 MHz
4
clocks
@ 1 MHz

## Slide 49
CPU | 4 MHz
RAM | 1 MHz
PPU | 4 MHz
VRAM | 2 MHz
4,194,304 Hz
1,048,576 Hz
4,194,304 Hz
2,097,152 Hz
System Clocks
“machine cycle” @ 1 MHz

## Slide 50
BOOT ROM
0 KB
64 KB
FE00
0000
8000
A000
C000
E000
ROM |  |  |  | Video RAM | External RAM | RAM |  | 
FF00
FF80
FEA0
OAM RAM |  | I/O | HRAM

## Slide 51
ROM |  |  |  |  | External RAM | RAM |  | 
0000
8000
32 KB?

## Slide 52
https://gekkio.fi/blog/
32 KB

## Slide 53
https://gekkio.fi/blog/
128 KB
MBC

## Slide 54
ROM Bank 0 |  | ROM Bank 1 |  |  | External RAM | RAM |  | 
0000
8000
ROM Bank 2 | 
ROM Bank 3 | 
ROM |  |  | 
4000

## Slide 55
BOOT ROM
0 KB
64 KB
FE00
0000
8000
A000
C000
E000
FF00
FF80
FEA0
OAM RAM |  | I/O | HRAM
ROM Bank 0 |  | ROM Bank 1-n |  | Video RAM | External RAM | RAM |  | 

## Slide 56
A000
C000
ROM Bank 0 |  | ROM Bank 1-n |  | Video RAM | External RAM 0 | RAM |  | 
External RAM 1
External RAM 2

## Slide 57
0 KB
64 KB
FE00
0000
8000
A000
C000
E000
ROM |  |  |  | Video RAM | External RAM | RAM |  | 
FF00
FF80
FEA0
OAM RAM |  | I/O | HRAM
BOOT ROM
0000-00FF

## Slide 58
https://www.youtube.com/watch?v=QyvBNhzshKQ

## Slide 59
ld c,a
ld b,$04
addr_0098:
push bc
rl c
rla
pop bc
rl c
rla
dec b
jr nz, addr_0098
ld (hl+),a
inc hl
ld (hl+),a
inc hl
ret
addr_00a8:
.db $ce,$ed,$66,$66,$cc,$0d,$00,$0b
.db $03,$73,$00,$83,$00,$0c,$00,$0d
.db $00,$08,$11,$1f,$88,$89,$00,$0e
.db $dc,$cc,$6e,$e6,$dd,$dd,$d9,$99
.db $bb,$bb,$67,$63,$6e,$0e,$ec,$cc
.db $dd,$dc,$99,$9f,$bb,$b9,$33,$3e
addr_00d8:
.db $3c,$42,$b9,$a5,$b9,$a5,$42,$3c
addr_00e0:
ld hl,$0104
ld de,$00a8
addr_00e6:
ld a,(de)
inc de
cp (hl)
jr nz,$fe
inc hl
ld a,l
cp $34
jr nz, addr_00e6
ld b,$19
ld a,b
addr_00f4:
add (hl)
inc hl
dec b
jr nz, addr_00f4
add (hl)
jr nz,$fe
ld a,$01
ld ($ff00+$50),a
ld sp,$fffe
xor a
ld hl,$9fff
addr_0007:
ld (hl-),a
bit 7,h
jr nz, addr_0007
ld hl,$ff26
ld c,$11
ld a,$80
ld (hl-),a
ld ($ff00+c),a
inc c
ld a,$f3
ld ($ff00+c),a
ld (hl-),a
ld a,$77
ld (hl),a
ld a,$fc
ld ($ff00+$47),a
ld de,$0104
ld hl,$8010
addr_0027:
ld a,(de)
call $0095
call $0096
inc de
ld a,e
cp $34
jr nz, addr_0027
ld de,$00d8
ld b,$08
addr_0039:
ld a,(de)
inc de
ld (hl+),a
inc hl
dec b
jr nz, addr_0039
ld a,$19
ld ($9910),a
ld hl,$992f
addr_0048:
ld c,$0c
addr_004a:
dec a
jr z, addr_0055
ld (hl-),a
dec c
jr nz, addr_004a
ld l,$0f
jr addr_0048
addr_0055:
ld h,a
ld a,$64
ld d,a
ld ($ff00+$42),a
ld a,$91
ld ($ff00+$40),a
inc b
addr_0060:
ld e,$02
addr_0062:
ld c,$0c
addr_0064:
ld a,($ff00+$44)
cp $90
jr nz, addr_0064
dec c
jr nz, addr_0064
dec e
jr nz, addr_0062
ld c,$13
inc h
ld a,h
ld e,$83
cp $62
jr z, addr_0080
ld e,$c1
cp $64
jr nz, addr_0086
addr_0080:
ld a,e
ld ($ff00+c),a
inc c
ld a,$87
ld ($ff00+c),a
addr_0086:
ld a,($ff00+$42)
sub b
ld ($ff00+$42),a
dec d
jr nz, addr_0060
dec b
jr nz, addr_00e0
ld d,$20
jr addr_0060
Init RAM
Init Sound
Set up Logo
Play Sound
Scroll logo
Scroll logo
Decode logo
Logo data
Compare logo
Checksum
header
Turn off ROM
Boot ROM

## Slide 61
Logo Hack

## Slide 62
Logo Hack
https://vimeo.com/user1849607
Is That a Demo in Your Pocket?
Gejmbåj
Oh!
20y
by Snorpung

## Slide 63
00f4 86 add (hl)
00f5 23 inc hl
00f6 05 dec b
00f7 20 fb jr nz, $00f4
00f9 86 add (hl)
00fa 20 fe jr nz, $fe
00fc 3e 01 ld a, $01
00fe e0 50 ld ($ff00+$50), a
Boot ROM
Game ROM
0100 00 nop
0101 c3 50 01 jp $0150
0104 ...
. ...
. ...
. ...
. ...
ld ($ff00+$50), a
Game ROM
. ...
. ...
. ...
. ...
. ...
. ...
. ...
. ...

## Slide 64
ROM Header |  | 
0100 - 0103 | Entry Point | nop, jp $0150
0104 - 0133 | Nintendo Logo | $CE, $ED, $66, $66, $CC, ...
0134 - 0143 | Title | “SUPER MARIOLAND”
013F - 0142 | Manufacturer Code | $00
0143 | CGB Flag | $00
0144 - 0145 | New Licensee Code | $00, $00
0146 | SGB Flag | $00
0147 | Cartridge Type | $01
0148 | ROM Size | $01
0149 | RAM Size | $00 \
014A | Destination Code | $00
014B | Old Licensee Code | $01
014C | Mask ROM Version number | $00
014D | Header Checksum | $9E $
014E - 014F | Global Checksum | $41, $6B

## Slide 65
0 KB
64 KB
FE00
0000
8000
A000
C000
E000
ROM |  |  |  | Video RAM | External RAM | RAM |  | 
FF00
FF80
FEA0
OAM RAM |  | I/O | HRAM

## Slide 66
 | FF00 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | FF0F
FF10 | P1 | SB | SC | DIV | TIMA | TMA | TAC |  |  |  |  |  |  |  |  | IF
 | NR10 | NR11 | NR12 | NR13 | NR14 |  | NR21 | NR22 | NR23 | NR24 | NR30 | NR31 | NR32 | NR33 | NR34 | 
 | NR41 | NR42 | NR43 | NR44 | NR50 | NR51 | NR52 |  |  |  |  |  |  |  |  | 
 | W0 | W1 | W2 | W3 | W4 | W5 | W6 | W7 | W8 | W9 | W10 | W11 | W12 | W13 | W13 | W14
 | LCDC | STAT | SCY | SCX | LY | LYC | DMA | BGP | OBP0 | OBP1 | WY | WX |  |  |  | 
 | BOOT |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
FFF0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | IE
HRAM

## Slide 68
Joypad Input

## Slide 70
→
←
↑
↓
P14
P15
P13
P12
P11
P10
Joypad Input |  | 
FF00 | P1 | Joypad (R/W)
5 | P15 | Select Button Keys
4 | P14 | Select Direction Keys
3 | P13 | Input Down / Start
2 | P12 | Input Up / Select
1 | P11 | Input Left / Button B
0 | P10 | Input Right / Button A

## Slide 71
Serial Data Transfer

## Slide 72
data →
data ←
←
→
clock
Serial Data Transfer |  | 
FF01 | SB | Serial transfer data (R/W)
FF02 | SC | Serial Transfer Control (R/W)
7 |  | Transfer Start Flag
0 |  | Clock Source (internal/external)
clock speeds | 
out | 8,192 kHz
in | 0 kHz – 524,288 kHz

## Slide 73
Timer

## Slide 74
Timer |  | 
FF04 | DIV | Divider Register (R/W)
FF05 FF06 FF07 | TIMA | Timer counter (R/W)
FF06 | TMA | Timer Modulo (R/W)
FF07 | TAC | Timer Control (R/W)
2 |  | Timer Start
1-0 |  | Input Clock Select
clock speeds |  | 
01 | 262,144 Hz | 4
10 | 65,536 Hz | 16
11 | 16,384 Hz | 64
00 | 4,096 Hz | 256

## Slide 75
Interrupt Controller

## Slide 76
RST $60
RST $58
RST $50
RST $48
RST $40
Interrupt Controller |  | 
FFFF | IE | Interrupt Enable (R/W)
4 |  | Joypad
3 |  | Serial
2 |  | Timer
1 |  | LCD STAT
0 |  | V-Blank
FF0F | IF | Interrupt Flag (R/W)
4 |  | Joypad
3 |  | Serial
2 |  | Timer
1 |  | LCD STAT
0 |  | V-Blank
Interrupt Controller |  | 

## Slide 77
Sound Controller

## Slide 78
Sound Controller |  | 
FF10 | NR10 | Channel 1 Sweep register (R/W)
FF11 | NR11 | Channel 1 Sound length/Wave pattern duty (R/W)
FF12 | NR12 | Channel 1 Volume Envelope (R/W)
FF13 | NR13 | Channel 1 Frequency lo (Write Only)
FF14 | NR14 | Channel 1 Frequency hi (R/W)
FF16 | NR21 | Channel 2 Sound Length/Wave Pattern Duty (R/W)
FF17 | NR22 | Channel 2 Volume Envelope (R/W)
FF18 | NR23 | Channel 2 Frequency lo data (W)
FF19 | NR24 | Channel 2 Frequency hi data (R/W)
FF1A | NR30 | Channel 3 Sound on/off (R/W)
FF1B | NR31 | Channel 3 Sound Length
FF1C | NR32 | Channel 3 Select output level (R/W)
FF1D | NR33 | Channel 3 Frequency's lower data (W)
FF1E | NR34 | Channel 3 Frequency's higher data (R/W)
FF20 | NR41 | Channel 4 Sound Length (R/W)
FF21 | NR42 | Channel 4 Volume Envelope (R/W)
FF22 | NR43 | Channel 4 Polynomial Counter (R/W)
FF23 | NR44 | Channel 4 Counter/consecutive; Inital (R/W)
FF24 | NR50 | Channel control / ON-OFF / Volume (R/W)
FF25 | NR51 | Selection of Sound output terminal (R/W)
FF26 | NR52 | Sound on/off

## Slide 79
T | L L |  |  |  | F | F | F
F | F | F | F | F | F | F | F
V | V | V | V | A | P | P | P
D | D | L | L | L | L | L | L
 | P | P | P | N | S | S | S
T | L |  |  |  | F | F | F
F | F | F | F | F | F | F | F
V | V | V | V | A | P | P | P
DF | D | L | L | L | L | L | L
T | L |  |  |  | F | F | F
F | F | F | F | F | F | F | F
 | V | V |  |  |  |  | 
L | L | L | L | L | L | L | L
T | L |  |  |  |  |  | 
S | S | S | S | W | D | D | D
V | V | V | V | A | P | P | P
 |  | L | L | L | L | L | L
4
3
2
1
0
Volume
Length
Frequency
Control
Sweep
Pulse A
Pulse B
Wave
Noise
NR10
NR20
NR30
NR40
NR41
NR42
NR43
NR44
NR34
NR33
NR32
NR31
NR21
NR11
NR12
NR22
NR23
NR13
NR14
NR24
Voice 1
Voice 2
Voice 3
Voice 4

## Slide 80
T | L |  |  |  | F | F | F
F | F | F | F | F | F | F | F
 | V | V |  |  |  |  | 
L | L | L | L | L | L | L | L
4
3
2
1
0
Volume
Length
Frequency
Control
Sweep
Wave
W0 | W1 | W2 | W3 | W4 | W5 | W6 | W7 | W8 | W9 | W10 | W11 | W12 | W13 | W13 | W14
FF30
Audio samples by @_drmr_

## Slide 81
T | L L |  |  |  | F | F | F
F | F | F | F | F | F | F | F
V | V | V | V | A | P | P | P
D | D | L | L | L | L | L | L
 | P | P | P | N | S | S | S
T | L |  |  |  | F | F | F
F | F | F | F | F | F | F | F
V | V | V | V | A | P | P | P
DF | D | L | L | L | L | L | L
4
3
2
1
0
Volume
Length
Frequency
Control
Sweep
Pulse A
Pulse B
12.5%
25%
50%
75%

## Slide 82
T | L L |  |  |  | F | F | F
F | F | F | F | F | F | F | F
V | V | V | V | A | P | P | P
D | D | L | L | L | L | L | L
 | P | P | P | N | S | S | S
T | L |  |  |  | F | F | F
F | F | F | F | F | F | F | F
V | V | V | V | A | P | P | P
DF | D | L | L | L | L | L | L
4
3
2
1
0
Volume
Length
Frequency
Control
Sweep
Pulse A
Pulse B

## Slide 83
T | L L |  |  |  | F | F | F
F | F | F | F | F | F | F | F
V | V | V | V | A | P | P | P
D | D | L | L | L | L | L | L
 | P | P | P | N | S | S | S
T | L |  |  |  | F | F | F
F | F | F | F | F | F | F | F
V | V | V | V | A | P | P | P
DF | D | L | L | L | L | L | L
4
3
2
1
0
Volume
Length
Frequency
Control
Sweep
Pulse A
Pulse B

## Slide 84
T | L |  |  |  |  |  | 
S | S | S | S | W | D | D | D
V | V | V | V | A | P | P | P
 |  | L | L | L | L | L | L
4
3
2
1
0
Volume
Length
Frequency
Control
Sweep
Noise

## Slide 85
T | L L |  |  |  | F | F | F
F | F | F | F | F | F | F | F
V | V | V | V | A | P | P | P
D | D | L | L | L | L | L | L
 | P | P | P | N | S | S | S
T | L |  |  |  | F | F | F
F | F | F | F | F | F | F | F
V | V | V | V | A | P | P | P
DF | D | L | L | L | L | L | L
T | L |  |  |  | F | F | F
F | F | F | F | F | F | F | F
 | V | V |  |  |  |  | 
L | L | L | L | L | L | L | L
T | L |  |  |  |  |  | 
S | S | S | S | W | D | D | D
V | V | V | V | A | P | P | P
 |  | L | L | L | L | L | L
4
3
2
1
0
Volume
Length
Frequency
Control
Sweep
Pulse A
Pulse B
Wave
Noise
NR10
NR20
NR30
NR40
NR41
NR42
NR43
NR44
NR34
NR33
NR32
NR31
NR21
NR11
NR12
NR22
NR23
NR13
NR14
NR24
NR50
NR51
NR52
A | L | L | L | B | R | R | R
N | W | 2 | 1 | N | W | 2 | 1
P |  |  |  | N | W | 2 | 1

## Slide 86
Little Sound Dj
Toriena & NNNNNNNNNN
Cheapshot - BrainFreeze Abortifacient remix (NNNNNNNNNN remix)

## Slide 87
Pixel Processing Unit

## Slide 88
Pixel Processing Unit |  |  |  |  | 
FF40 | LCDC | LCD Control (R/W) | FF42 | SCY | Scroll Y (R/W)
7 |  | LCD Display Enable | FF43 | SCX | Scroll X (R/W)
6 |  | Window Tile Map Address | FF44 | LY | LCDC Y-Coordinate (R)
5 |  | Window Enable | FF45 | LYC | LY Compare (R/W)
4 |  | BG & Window Tile Data Address | FF46 | DMA | DMA Transfer and Start Address (W)
3 |  | BG Tile Map Address | FF47 | BGP | BG Palette (R/W)
2 |  | OBJ Size | FF48 | OBP0 | Object Palette 0 (R/W)
1 |  | OBJ Enable | FF49 | OBP1 | Object Palette 1 (R/W)
0 |  | BG Enable | FF4A | WY | Window Y Position (R/W)
FF41 | STAT | LCDC Status (R/W) | FF4B | WX | Window X Position (R/W)
6 |  | LYC=LY Interrupt |  |  | 
5 |  | Mode 2 OAM Interrupt |  |  | 
4 |  | Mode 1 V-Blank Interrupt |  |  | 
3 |  | Mode 0 H-Blank Interrupt |  |  | 
2 |  | LYC=LY Flag |  |  | 
1-0 |  | Mode |  |  | 

## Slide 90
Specifications
160x144 pixels
4 shades of gray
8x8 pixel tile-based, 20x18 tiles
40 sprites (10 per line)
8 KB VRAM

## Slide 92
20x18 Background Tiles

## Slide 93
20x18 Background Tiles

## Slide 94
20x18 Background Tiles

## Slide 95
20x18 Background Tiles

## Slide 96
20x18 Background Tiles

## Slide 97
02
FF
73
8C
65
9A
48
B6
12
EC
26
D8
CE
B0
60
80
0
1
0
1
0
1
0
1
0
1
0
1
1
1
0
1
0
1
1
0
1
0
1
0
0
1
0
1
1
0
1
0
0
1
1
0
1
0
0
1
0
1
1
0
0
1
1
0
0
1
1
0
0
1
0
1
1
0
0
1
0
1
0
0
0
1
0
1
0
1
1
0
0
1
0
1
1
0
0
0
0
1
0
1
1
0
0
1
0
1
1
0
1
0
0
0
1
1
1
0
0
1
0
1
1
0
1
0
1
0
0
0
0
1
1
0
1
0
0
0
0
0
0
0
0
0
0
0
16 bytes
per tile
8x8 Pixel Tiles
0
1
1
0
0
0
1
1

## Slide 98
0
1
1
0
0
0
1
1
FF47 | BGP | BG Palette (R/W)
6-7 |  | Color for 11
4-5 \ |  | Color for 10
2-3 |  | Color for 01
0-1 |  | Color for 00
01
10
11
00
0
1
1
0
0
0
1
1
0
0
1
1
0
1
1
0
0
0
1
1
0
1
1
0
Background Palettes
…
0
0
1
1
0
1
1
0

## Slide 99
Tetris
256 tiles
Background Tile Data

## Slide 100
Zelda
Background Tile Data

## Slide 101
Super Mario Land
Background Tile Data

## Slide 102
Background Tile Data

## Slide 103
20 tiles
18 tiles
All Star Tennis

## Slide 104
32 tiles
32 tiles
Background Map
Scrolling
256x256
pixels
FF42 | SCY | Scroll Y (R/W)
FF43 | SCX | Scroll X (R/W)
Notes: All Star Tennis

## Slide 110
FF40 | LCDC | LCD Control (R/W)
5 |  | Window Enable
FF4A | WY | Window Y Position (R/W)
FF4B | WX | Window X Position (R/W)
Window
Notes: window shares palette with background
“Race Days” animates the window!

## Slide 111
Window
Notes: Project S-11
better example: Trax!

## Slide 112
Position X | 0x__
Position Y | 0x__
Tile Number | 0x__
Priority | _
Flip X | ☐
Flip Y | ☐
Palette | _
OAM Entry
FF40 | LCDC | LCD Control (R/W)
1 |  | OBJ Enable
Sprites
Notes: x-8
y-16

## Slide 113
FF40 | LCDC | LCD Control (R/W)
1 |  | OBJ Enable
Position X | 0x__
Position Y | 0x__
Tile Number | 0x__
Priority | _
Flip X | ☐
Flip Y | ☐
Palette | _
OAM Entry
0x08
0x04
0x00
0x08
0x10
Sprites
0x4D
0x78
Notes: x-8
y-16

## Slide 114
Position X | 0x4D
Position Y | 0x78
Tile Number | 0x__
Priority | _
Flip X | ☐
Flip Y | ☐
Palette | _
OAM Entry

## Slide 115
Position X | 0x4D
Position Y | 0x78
Tile Number | 0x__
Priority | _
Flip X | ☐
Flip Y | ☐
Palette | _
OAM Entry

## Slide 116
Position X | 0x4D
Position Y | 0x78
Tile Number | 0x__
Priority | _
Flip X | ☐
Flip Y | ☐
Palette | _
0x90
OAM Entry

## Slide 117
Position X | 0x4D
Position Y | 0x78
Tile Number | 0x90
Priority | _
Flip X | ☐
Flip Y | ☐
Palette | _
  ☒
  ☒
  ☒
OAM Entry

## Slide 118
Position X | 0x4D
Position Y | 0x78
Tile Number | 0x90
Priority | _
Flip X | ☐
Flip Y | ☐
Palette | _
OAM Entry
Palette 0
Palette 1
1
0
FF48 | OBP0 | Object Palette 0 (R/W)
FF49 | OBP1 | Object Palette 1 (R/W)

## Slide 119
BG Palette
0
1
2
3
Position X | 0x4D
Position Y | 0x78
Tile Number | 0x90
Priority | _
Flip X | ☐
Flip Y | ☐
Palette | 0
OAM Entry
1
0

## Slide 120
Sprite/Sprite Priority

## Slide 121
40 sprites total

## Slide 123
10 sprites per line

## Slide 124
OAM RAM
Position X | 0x4D
Position Y | 0x78
Tile Number | 0x90
Priority | 1
Flip X | ☐
Flip Y | ☐
Palette | 0
OAM Entry
Position Y
Position X
Tile Number
Flags
FE00
0
FE04
FE08
FE0C
FE10
FE9C
…
1
2
3
4
39

## Slide 125
FF40 | LCDC | LCD Control (R/W)
2 |  | OBJ Size
8x8 or 8x16

## Slide 126
LCD Off
LCD On (00)
Background (01)
Window (10)
Off | 00 | 01 | 10 | 11
FF40 | LCDC | LCD Control (R/W)
7 |  | LCD Display Enable
5 |  | Window Enable
1 |  | OBJ Enable
0 |  | Background Enable
Layers
Notes: there is just a single mode with 3 components

## Slide 127
8000
9000
8800
9800
Sprite Tiles
BG Tiles
BG Map
Window Map
4 KB
4 KB
1 KB
1 KB
256 tiles x 16 bytes
256 tiles x 16 bytes
32 x 32 indexes
32 x 32 indexes
?
?
VRAM Memory Map

## Slide 128
8000
9000
8800
9800
BG Tiles
BG Map
Window Map
Sprite Tiles
FF40 | LCDC | LCD Control (R/W)
6 |  | Window Tile Map Address
4 |  | BG & Window Tile Data Address
3 |  | BG Tile Map Address
VRAM Memory Map

## Slide 129
8000
8800
9000
9800
Sprite Tiles
BG Tiles

## Slide 130
Vertical Timing
Pixel Processing Unit

## Slide 131
Timing

## Slide 132
Timing

## Slide 135
SCX = 0
SCX = 23
SCX = ?
SCX = 0
LYC = 8
LYC = 42
LYC = 88
LYC = 8
FF41 | STAT | LCDC Status (R/W)
6 |  | LYC=LY Interrupt
2 |  | LYC=LY Flag
FF44 | LY | LCDC Y-Coordinate (R)
FF45 | LYC | LY Compare (R/W)
LYC Interrupt

## Slide 136
LCDC.WINON = 1
LCDC.WINON = 0
LCY = 0
LCY = 40

## Slide 138
Changing SCX

## Slide 139
26
30
6
0
16
29
22
14
18
28
SCX =
Changing SCX

## Slide 141
Changing SCX

## Slide 142
0
60
34
24
16
11
7
4
3
2
1
SCX =
01
01
00
01
00
01
00
01
00
01
00
= PAL
Changing SCX

## Slide 145
Horizontal Timing
Pixel Processing Unit

## Slide 146
OAM
Search
Pixel Transfer
H-Blank
43 clocks
51 clocks
20 clocks
144
lines
V-Blank
10
lines
= 17,556 clocks per screen
114 x 154
= 59.7 Hz refresh rate
1,048,576 / 17,556
FF41 | STAT | LCDC Status (R/W)
5 |  | Mode 2 OAM Interrupt
4 |  | Mode 1 V-Blank Interrupt
3 |  | Mode 0 H-Blank Interrupt
1-0 |  | Mode
FF0F | IF | Interrupt Flag (R/W)
0 |  | V-Blank
FFFF | IE | Interrupt Enable (R/W)
0 |  | V-Blank
0
3
2
1
PPU Timing

## Slide 147
OAM
Search
Pixel Transfer
H-Blank
V-Blank

## Slide 148
OAM
Search
Pixel Transfer
H-Blank
V-Blank
o | o | o | o |  |  | o | o | o | o | o | o | o |  | o | o | o | o | o | o | o | o |  | o | o | o |  |  |  | o | o |  |  |  |  |  |  |  |  | 
o | o | o | o | o | o | o |  |  | 
all Sprites
visible Sprites
oam.x ≠ 0
∧ LY + 16 ≥ oam.y
∧ LY + 16 < oam.y + h
OAM Search

## Slide 149
ld a, (hl+)
ld a, (hl-)
ld (hl+), a
ld (hl-), a
OAM Search CPU Bug
inc bc
inc de
inc hl
inc sp
dec bc
dec de
dec hl
dec sp
r16 inc/dec
FE00 ≤ r16 ≤ FEFF
during OAM search
will trash OAM RAM

## Slide 150
PPU
CPU
RAM
8 KB
OAM RAM __ _
Video
RAM
8 KB
160 B
VRAM Access

## Slide 151
OAM
Search
Pixel Transfer
H-Blank
43 clocks
51 clocks
20 clocks
144
lines
V-Blank
10
lines
OAM
Search
H-Blank
V-Blank
Pixel Transfer
VRAM
Access
OK
VRAM
Access
BAD
VRAM Access

## Slide 152
OAM
Search
Pixel Transfer
H-Blank
43 clocks
51 clocks
20 clocks
144
lines
V-Blank
10
lines
OAM
Search
H-Blank
V-Blank
Pixel Transfer
OAM
Search
H-Blank
V-Blank
Pixel Transfer
OAM
Access
OK
OAM
Access
BAD
OAM Access

## Slide 153
OAM
Search
Pixel Transfer
H-Blank
V-Blank
Move background map
Game Timing
1,140 clocks
Player movement
Enemy AI
Enemy movement
Projectile movement
Collisions
Score
*
*
*
* on shadow OAM
*
Copy shadow OAM to OAM

## Slide 154
ld ($FF46), a
ROM | Video RAM | External RAM | RAM | OAM | I/O | HRAM
0000
8000
A000
C000
FE00
FF00
FF80
OAM DMA
FF46 | DMA | DMA Transfer and Start Address (W)
ld ($FF46), a
ld a, 40
wait: dec a
jr nz, wait
160 clocks

## Slide 155
Pixel Pipeline
Pixel Processing Unit
Fine Print
A lot of this information is based on experiments with a custom Game Boy emulator. The results match Game Boy timing traces but could not be verified yet.
Also, some information on the following slides is slightly simplified.

## Slide 156
Pixel FIFO
LCD

## Slide 157
Pixel FIFO
LCD

## Slide 158
Pixel FIFO
LCD

## Slide 159
Pixel FIFO
LCD
Read Tile #
Read Data 0
Read Data 1
9802
Fetch

## Slide 160
Pixel FIFO
LCD
Read Tile #
Read Data 0
Read Data 1
04
9802
Background Map
9802: 04 EA 2E
Fetch

## Slide 161
Pixel FIFO
LCD
Read Tile #
Read Data 0
Read Data 1
04
9802
02
Tile Data
8040: 02 FE 6A
Fetch

## Slide 162
LCD
Pixel FIFO
Fetch
Read Tile #
Read Data 0
Read Data 1
04
9802
02
FE
9803
Tile Data
8040: 02 FE 6A

## Slide 163
LCD
Pixel FIFO
Fetch
Read Tile #
Read Data 0
Read Data 1
9803
FIFO | Fetch
Push | 

## Slide 164
LCD
Pixel FIFO
Fetch
Read Tile #
Read Data 0
Read Data 1
9803
FIFO | Fetch
Push | 
FIFO | Fetch
Push | Read Tile #
Push | 
60

## Slide 165
FIFO | Fetch
Push | Read Tile #
Push | 
Push | 
LCD
Pixel FIFO
Fetch
Read Tile #
Read Data 0
Read Data 1
9803
FIFO | Fetch
Push | Read Tile #
Push | 
60

## Slide 166
LCD
Pixel FIFO
Fetch
Read Tile #
Read Data 0
Read Data 1
9803
FIFO | Fetch
Push | Read Tile #
Push | 
60
FIFO | Fetch
Push | Read Tile #
Push | 
Push | 
73
FIFO | Fetch
Push | Read Tile #
Push | 
Push | Read Data 0
Push | 

## Slide 167
FIFO | Fetch
Push | Read Tile #
Push | 
Push | Read Tile #
Push | 
Push | 
LCD
Pixel FIFO
Fetch
Read Tile #
Read Data 0
Read Data 1
9803
FIFO | Fetch
Push | Read Tile #
Push | 
60
FIFO | Fetch
Push | Read Tile #
Push | 
Push | Read Data 0
Push | 
FIFO | Fetch
Push | Read Tile #
Push | 
Push | Read Data 0
Push | 
73

## Slide 168
LCD
Pixel FIFO
Fetch
Read Tile #
Read Data 0
Read Data 1
FIFO | Fetch
Push | Read Tile #
Push | 
60
FIFO | Fetch
Push | Read Tile #
Push | 
Push | 
FIFO | Fetch
Push | Read Tile #
Push | 
Push | Read Tile #
Push | 
73
FIFO | Fetch
Push | Read Tile #
Push | 
Push | Read Data 0
Push | 
Push | 
8C
9803
9804
FIFO | Fetch
Push | Read Tile #
Push | 
Push | Read Data 0
Push | 
Push | Read Data 1
Push | 

## Slide 169
LCD
Pixel FIFO
Fetch
Read Tile #
Read Data 0
Read Data 1
9804
FIFO | Fetch
Push | Read Tile #
Push | 
Push | Read Tile #
Push | 
Push | Read Tile #
Push | 
FIFO | Fetch
Push | Read Tile #
Push | 
Push | Read Data 0
Push | 
Push | Read Data 1
Push | 
Push | 
FIFO | Fetch
Push | Read Tile #
Push | 
Push | Read Data 0
Push | 
Push | Read Data 1
Push | 

## Slide 170
LCD
Pixel FIFO
Fetch
Read Tile #
Read Data 0
Read Data 1
9804
FIFO | Fetch
Push | Read Tile #
Push | 
Push | Read Data 0
Push | 
Push | Read Data 1
Push | 
Push | 
FIFO | Fetch
Push | Read Tile #
Push | 
Push | Read Data 0
Push | 
Push | Read Data 1
Push | 
Push | Idle
Push | 
4 MHz
2 MHz

## Slide 171
pushes one pixel per clock
pauses unless it contains more than 8 pixels
3 clocks to fetch 8 pixels
pauses in 4th clock unless space in FIFO
FIFO
Fetch
4 MHz
2 MHz

## Slide 172
LCD
Pixel FIFO
Horizontal Scrolling
SCX = 3

## Slide 173
LCD
Pixel FIFO
Horizontal Scrolling
SCX = 3

## Slide 174
LCD
Pixel FIFO
Horizontal Scrolling
SCX = 3

## Slide 175
LCD
Pixel FIFO
Horizontal Scrolling
SCX = 3

## Slide 176
Fetch
Read Tile #
Read Data 0
Read Data 1
9816
Pixel FIFO
LCD
End of Line
x = 160
End of Line
H-Blank

## Slide 177
LCD
Pixel FIFO
WX = 26
Window
Fetch
Read Tile #
Read Data 0
9804
9C00
Read Data 1
Window

## Slide 178
LCD
Pixel FIFO
Fetch
Read Tile #
Read Data 0
9804
FE02
Read Data 1
Sprites
oam[0].x = 26
OBJ
oam[1].x = 40
OBJ

## Slide 179
t
first pixel of the line
start of window
pipeline cleared
FIFO paused
Fetcher reads window tiles
Game Boy / LCD
FIFO resumed
Commodore 64 / CRT
t
first pixel of the line
last pixel of the line
always exactly 40 clocks
43+ clocks
last pixel of the line

## Slide 180
OAM
Search
Pixel Transfer
H-Blank
43 clocks
51 clocks
20 clocks
144
lines
V-Blank
10
lines
43+ clocks
51- clocks

## Slide 181
Read Tile #
Read Data 0
Read Data 1
LCD
Pixel FIFO
Fetch
9804
FE02
Pixel Mixing

## Slide 182
00 | 11 | 11 | 01 | 11 | 01 | 11 | 00
S1 | S1 | S1 | S1 | S1 | S1 | S1 | S1
P0
10 | 01 | 01 | 10 | 10 | 11 | 01 | 10 | 00 |  |  |  |  |  |  | 
BG | BG | BG | BG | BG | BG | BG | BG | BG |  |  |  |  |  |  | 
LCD
Pixel FIFO
Fetch
Read Tile #
Read Data 0
9804
Read Data 1
FE02
10 | 01 | 01 | 10 | 10 | 11 | 01 | 10
BG | BG | BG | BG | BG | BG | BG | BG
Pixel Mixing

## Slide 183
10 | 11 | 11 | 01 | 11 | 01 | 11 | 10
BG | S1 | S1 | S1 | S1 | S1 | S1 | BG
10 | 01 | 01 | 10 | 10 | 11 | 01 | 10
BG | BG | BG | BG | BG | BG | BG | BG
00 | 11 | 11 | 01 | 11 | 01 | 11 | 00
S1 | S1 | S1 | S1 | S1 | S1 | S1 | S1
P0
10
BG
11
S1
11
S1
01
S1
11
S1
01
S1
11
S1
10
BG
10
BG
11
S1
10
BG
11
S1
01
S1
11
S1
01
S1
11
S1
Pixel Mixing

## Slide 184
10 | 11 | 11 | 01 | 11 | 01 | 11 | 10
BG | S1 | S1 | S1 | S1 | S1 | S1 | BG
01 | 01 | 01 | 01 | 01 | 01 | 01 | 01
S0 | S0 | S0 | S0 | S0 | S0 | S0 | S0
P0
01
S0
11
S1
01
S0
11
S1
01
S1
11
S1
01
S1
11
S1
01
S0
11
S1
11
S1
01
S1
11
S1
01
S1
11
S1
01
S0
Pixel Mixing

## Slide 185
01 | 11 | 11 | 01 | 11 | 01 | 11 | 01 | 00 |  |  |  |  |  |  | 
S0 | S1 | S1 | S1 | S1 | S1 | S1 | S0 | BG |  |  |  |  |  |  | 
LCD
Pixel FIFO
S0
00
01
10
11
S1
00
01
10
11
BG
00
01
10
11
Applying the Palettes

## Slide 186
11 | 11 | 01 | 11 | 01 | 11 | 01 | 00 | 01 | 11 | 01 | 10 | 10 | 11 | 00 | 01
S1 | S1 | S1 | S1 | S1 | S1 | S0 | BG | BG | BG | BG | BG | BG | BG | BG | BG
LCD
Pixel FIFO
S0
00
01
10
11
S1
00
01
10
11
BG
00
01
10
11
Applying the Palettes

## Slide 187
11 | 01 | 11 | 01 | 11 | 01 | 00 | 01 | 11 | 01 | 10 | 10 | 11 | 00 | 01 | 
S1 | S1 | S1 | S1 | S1 | S0 | BG | BG | BG | BG | BG | BG | BG | BG | BG | 
LCD
Pixel FIFO
S0
00
01
10
11
S1
00
01
10
11
BG
00
01
10
11
Applying the Palettes

## Slide 188
S0
00
01
10
11
S1
00
01
10
11
BG
00
01
10
11
01 | 11 | 01 | 11 | 01 | 00 | 01 | 11 | 01 | 10 | 10 | 11 | 00 | 01 |  | 
S1 | S1 | S1 | S1 | S0 | BG | BG | BG | BG | BG | BG | BG | BG | BG |  | 
LCD
Pixel FIFO
S0
00
01
10
11
S1
00
01
10
11
BG
00
01
10
11
Colorization

## Slide 189
11 | 01 | 11 | 01 | 00 | 01 | 11 | 01 | 10 | 10 | 11 | 00 | 01 |  |  | 
S1 | S1 | S1 | S0 | BG | BG | BG | BG | BG | BG | BG | BG | BG |  |  | 
LCD
Pixel FIFO
S0
00
01
10
11
S1
00
01
10
11
BG
00
01
10
11
Colorization

## Slide 190
01 | 11 | 01 | 00 | 01 | 11 | 01 | 10 | 10 | 11 | 00 | 01 |  |  |  | 
S1 | S1 | S0 | BG | BG | BG | BG | BG | BG | BG | BG | BG |  |  |  | 
LCD
Pixel FIFO
S0
00
01
10
11
S1
00
01
10
11
BG
00
01
10
11
Colorization

## Slide 191
End of the technical part

## Slide 192
Development

## Slide 193
https://github.com/bentley/rgbds
$ rgbasm
Usage: rgbasm [-hv] [-b chars] [-Dname[=value]] [-g chars] [-i path]
[-o outfile] [-p pad_value] file.asm
$ rgblink
usage: rgblink [-t] [-m mapfile] [-n symfile] [-o outfile] [-p pad_value]
[-s symbol] file [...]
$ rgbfix
usage: rgbfix [-Ccjsv] [-i game_id] [-k licensee_str] [-l licensee_id]
[-m mbc_type] [-n rom_version] [-p pad_value] [-r ram_size]
[-t title_str] file
Rednex Game Boy Development System

## Slide 194
http://bgb.bircd.org/
BGB Emulator/Debugger

## Slide 195
https://krikzz.com/
Everdrive GB

## Slide 196
Game Boy Camera

## Slide 198
http://www.blood-is-red.de

## Slide 199
http://www.blood-is-red.de

## Slide 213
Lisa @ellduin
Dominik @monkeydom
Orlando Bassotto
Felix @tmbinc
bunnie @bunniestudios
@_drmr_
Costis Sideris

## Slide 214
The Ultimate Talk Series
The Ultimate
Commodore 64 Talk
Michael Steil
25C3
2008
The Ultimate
Atari 2600 Talk
Sven Oliver ('SvOlli') Moll
26C3
2009
The Ultimate
Galaksija Talk
Tomaž Šolc
29C3
2012
?
The Ultimate
Game Boy Talk
Michael Steil
33C3
2016
The Ultimate
Amiga 500 Talk
rahra
32C3
2015

## Slide 215
The Ultimate Talk Series
The Ultimate
Commodore 64 Talk
Michael Steil
25C3
2008
The Ultimate
Atari 2600 Talk
Sven Oliver ('SvOlli') Moll
26C3
2009
The Ultimate
Galaksija Talk
Tomaž Šolc
29C3
2012
The Ultimate
Game Boy Talk
Michael Steil
33C3
2016
The Ultimate
Amiga 500 Talk
rahra
32C3
2015
?

## Slide 216
?
The Ultimate Talk Series
?

## Slide 217
?
?
I nominate for 34C3
The Ultimate
Acorn Archimedes Talk
Dominik Wagner
The Ultimate
Super Nintendo Talk
Jannis Harder

## Slide 218
I nominate for 34C3
The Ultimate
Acorn Archimedes Talk
Dominik Wagner
The Ultimate
Super Nintendo Talk
Jannis Harder
Thank you!